SECTION 04 20 00

MASONRY ACCESSORIES – Weep Vents

GENERAL

SECTION INCLUDES

Weep Vents.

RELATED SECTIONS

Section 04 20 00 – Clay Unit Masonry:  Cavity wall construction of brick veneer.

REFERENCES

ASTM E 84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

SUBMITTALS

Submit under provisions of Section 01 33 00.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

QUALITY ASSURANCE

Manufacturer Qualifications:  Minimum 2 years production of similar products.

Installer Qualifications:  Minimum 2 years experience as a masonry installer.

DELIVERY, STORAGE, AND HANDLING

Store products in manufacturer's unopened packaging until ready for installation.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:  Keene Building Products; PO Box 241353, Mayfield Heights, Ohio 44124.  Toll Free Tel: (877) 514-5336, Tel: (440) 605-1020.  Fax: (440) 605-1120.  Email: info@keeneBuilding.com.  Web: http://www.KeeneBuilding.com.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01 25 00.

WEEP VENTS

Weep Vents:  Polyester non-woven mesh vent that is placed in the vertical head joints approximately every two feet to create a space for moisture to drain and vent in a brick cavity wall.

Product: Driwall™ Weep Vents as manufactured by Keene Building Products.

Description:

2.5” x 3.5” x 0.375”

Polyester

EXECUTION

INSTALLATION

  - Place weep vents in open head joints of cavity wall located immediately above ledges and flashing, spaced 24 inches apart, unless otherwise shown.

END OF SECTION